## Slide 1
Get two signal blocks of length N from both signal streams (No MAC operations)
Process the FFT of the combined signal blocks as complex input ( MACs)
Extract the FFT of the individual signals
(4N MACs)
Multiply the UPR and signal responses to get the transform of both outputs
(2N MACs)
Process the IFFT of the combined y transforms as complex input
( MACs)
Take the real and imaginary parts as the output blocks, but discard the first M samples
(No MAC operations)
N-M samples of output are generated per output stream, so 2(N-M) output samples are generated total
OVERLAP-SAVE

## Slide 2
Get two signal blocks of length (N-M) from both signal streams and zero-pad them to length N
(No MAC operations)
Process the FFT of the combined signal blocks as complex input ( MACs)
Extract the FFT of the individual signals
(4N MACs)
Multiply the UPR and signal responses to get the transform of both outputs
(2N MACs)
Process the IFFT of the combined y transforms as complex input
( MACs)
Take the real and imaginary parts as the output blocks, add them to the output vector
(No MAC operations)
N-M samples of output are generated per output stream, so 2(N-M) output samples are generated total
OVERLAP-ADD